## Slide 1: Unit -5 Process-to- Process Delivery UDP, TCP, and SCTP

## Slide 2: INTRODUCTION
oThe transport layer is responsible for the delivery of a message from one process to another
oThe transport layer header must include a service – point –address in the OSI model or port number in the TCP/IP (internet model)
oThe Internet model has three protocols at the transport layer:
UDP, TCP, and SCTP.
UDP: Is the simplest of the three.
TCP: A complex transport layer protocol.
SCTP: The new transport layer protocol that is designed for specific applications such as multimedia. a new reliable, message-oriented transport layer protocol that combines the best features of UDP and TCP

## Slide 3: PROCESS-TO-PROCESS DELIVERY
oThe Data link layer is responsible for delivery of frames between nodes over a link node to node delivery using a MAC address to choose one node among several.
The Network layer is responsible for delivery of datagrams between two hosts host to host delivery using an IP address to choose one host among millions.
Real communication takes place between two processes (application programs). We need process-to-process delivery.
oWe need a mechanism to deliver data from one of process running on the source host to the corresponding process running on the destination host.
oThe Transport layer is responsible for process-to-process . We need a port
number, to choose among multiple processes running on the destination host.

## Slide 4: TYPES OF DATA DELIVERIES

## Slide 5: CLIENT/SERVER PARADIGM
o process-to-process communication can be achieved through client/server
oA process on the local host, called a client, needs services from a process usually on the remote host, called a server.
oBoth processes (client and server) have the same name.
oFor example, to get the day and time from a remote machine, we need a Daytime client process running on the local host and a Daytime server process running on a remote machine.
oA remote computer can run several server programs at the same time, just as local computers can run one or more client programs at the same time.

## Slide 6: PORT NUMBER
oIn the Internet model, the port numbers are 16-bit integers between 0 and 65,535.
oThe client program defines itself with a port number, chosen randomly by the transport layer software running on the client host
oThe server process must also define itself with a port number This port
number, however, cannot be chosen randomly
oThe Internet uses port numbers for servers called well- known port numbers.
oEvery client process knows the well-known port number of the corresponding server process
o For example, while the Daytime client process, can use an ephemeral (temporary) port number 52,000 to identify itself, the Daytime server process must use the well-known (permanent) port number 13.

## Slide 8: IP ADDRESSES VERSUS PORT NUMBERS
IP addresses and port numbers play different roles in selecting the final
destination of data.
The destination IP address defines the host among the different hosts
After the host has been selected, the port number defines one of the processes on this particular host

## Slide 9: SOCKET ADDRESSES
o Process-to-process delivery needs two identifiers, IP address and the port
number, at each end to make a connection.
oThe combination of an IP address and a port number is called a socket address.
oA transport layer protocol needs a pair of socket addresses: the client socket address and the server socket address.
oThese four pieces of information are part of the IP header and the transport layer protocol header.
The IP header contains the IP addresses; the UDP or TCP header contains the port numbers.

## Slide 10: CONNECTIONLESS VERSUS CONNECTION-ORIENTED SERVICE
oA transport layer protocol can either be connectionless or connection-
oriented.
oConnectionless Service
In a connectionless service, the packets are sent from one party to another with no need for connection establishment or connection release.
The packets are not numbered; they may be delayed or lost or may arrive out of sequence.
There is no acknowledgment.
oConnection Oriented Service
In a connection-oriented service, a connection is first established between the sender and the receiver.
Data are transferred.
At the end, the connection is released. ( virtual connection , not a physical
connection)

## Slide 11: R E L I AB LE VERSUS U N R E L I A B L E
oThe transport layer service can be reliable or unreliable.
oIf the application layer program needs reliability, we use a reliable transport layer protocol by implementing flow and error control at the transport layer. This means a slower and more complex service.
oOn the other hand, if the application program does not need reliability then an unreliable protocol can be used.
Note
oUDP is connectionless and unreliable;
oTCP and SCTP are connection oriented and reliable.
These three protocols can respond to the demands of the
application layer programs.

## Slide 12
ERROR CONTROL
If the data link layer is reliable and has flow and error control, do we need this at the transport layer, too? Yes

## Slide 13
UDP
UDP is located between the application layer and the IP layer, and serves as the intermediary between the application programs and the network operations.

## Slide 14
TCP/IP PROTOCOL SUITE
16
Figure 14.1
Position of UDP in the TCP/IP protocol suite

## Slide 15: 1. USER DATAGRAM PROTOCOL (UDP )
oUDP is a connectionless, unreliable transport protocol.
oIt does not add anything to the services of IP (very simple) except to provide process-to process communication instead of host-to-host communication.
o(when to use it?) If a process wants to send a small message and does not care much about reliability, it can use UDP.
https://www.youtube.com/watch?v=blV7WUZpkCE
UDP packets, called user datagrams, have a fixed size header of 8 bytes.
UDP
called
packets,
user
datagrams,
have
fixed-size of 8
a header bytes.

## Slide 16: U D P CHARACTERISTICS
End-to-End: an application sends/receives data to/from another application.
Connectionless: Application does not need to preestablish communication before sending data; application does not need to terminate communication when finished.
Message-oriented: application sends/receives individual messages (UDP datagram), not packets.
Best-effort: same best-effort delivery semantics as IP. I.e. message can be
lost, duplicated, and corrupted.
Arbitrary interaction: application communicates with many or one other applications.
Operating system independent: identifying application does not depend on O/S.

## Slide 17: U DP DATAGRAM FORMAT
Source Port - 16 bit port number
Destination Port - 16 bit port number
Length (of UDP header + data) - 16 bit count of octets
UDP checksum - 16 bit field. if 0, then there is no checksum, else it is a checksum
over a pseudo header + UDP data area

## Slide 18: 2. TRANSMISSION CONTROL PROTOCOL(TCP)
oTCP, like UDP, is a process-to-process (program-to- program) protocol uses port numbers.
oUnlike UDP, TCP is a connection oriented protocol; it creates a virtual connection between two TCPs to send data.
oTCP uses flow and error control mechanisms at the transport level.

## Slide 19
23-3 TCP
TCP is a connection-oriented protocol; it creates a virtual connection between two TCPs to send data. In addition, TCP uses flow and error control mechanisms at the transport level.
TCP Services TCP Features
Segment
A TCP Connection
Flow Control
Error Control
Topics discussed in this section:

## Slide 20
Table 23.2 Well-known ports used by TCP

## Slide 21
Figure 23.13 Stream delivery

## Slide 22
Figure 23.14 Sending and receiving buffers

## Slide 23
Figure 23.15 TCP segments

## Slide 24
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with a randomly generated number.
Note

## Slide 25
The following shows the sequence number for each segment:
Example 23.3

## Slide 26
The value in the sequence number field of a segment defines the
number of the first data byte contained in that segment.
Note

## Slide 27
The value of the acknowledgment field in a segment defines
the number of the next byte a party expects to receive.
The acknowledgment number is cumulative.
Note

## Slide 28
Figure 23.16 TCP segment format

## Slide 29: TCP SEGMENT FORMAT
Reserved. This is a 6-bit field reserved for future use.
Control: This field defines 6 different control bits or flags. One or more of these bits can be set at a time. These bits enable flow control, connection establishment and termination, connection abortion, and the mode of data transfer in TCP

## Slide 31
Figure 23.18 Connection establishment using three-way handshaking

## Slide 32
A SYN segment cannot carry data, but it consumes one sequence number.
Note

## Slide 33
A SYN + ACK segment cannot carry data, but does consume one sequence number.
Note

## Slide 34
An ACK segment, if carrying no data, consumes no sequence number.
Note

## Slide 35
Figure 23.19 Data transfer

## Slide 36
Figure 23.20 Connection termination using three-way handshaking

## Slide 37
Byte numbering is used for flow and error control. For example: if the random number happens to be 1057 and the total data to be sent are 6000 bytes, the bytes are numbered from 1057 to 7056.
After the bytes have been numbered, TCP assigns a sequence number to each segment that is being sent.
The sequence number for each segment is the number of the first byte carried in that segment

## Slide 38: Acknowledgment Number
Each party uses an acknowledgment number to confirm the bytes it has received.
The acknowledgment number defines the number of the next byte that the party expects to receive.

## Slide 39: B. T C P S E G M E N T F O R M AT

## Slide 40: TCP Segment Format
The segment consists of a 20-60-byte header. Source port address:
This is a 16-bit field , it defines the port number of the application program in the
host that is sending the segment.
Destination port address:
This is a 16-bit field, it defines the port number of the application program in the host that is receiving the segment.
Sequence number: This 32-bit field defines the number assigned to the first byte of
data contained in this segment.
Acknowledgment number: This 32 bit field defines the number of the next byte a party expects to receive.
Header length: A 4-bit field that indicates the number of 4-byte words in the TCP header. The length of the header can be between 20 and 60 bytes. Therefore, the value of this field can be between 5 (5 x 4 =20) and 15 (15 x 4 =60).

## Slide 41
Reserved. This is a 6-bit field reserved for future use.
Control: This field defines 6 different control bits or flags. One or more of these bits can be set at a time. These bits enable flow control, connection establishment and termination, connection abortion, and the mode of data transfer in TCP
TCP SEGMENT FORMAT

## Slide 43
Urgent data :
oThe data are presented from the application program to TCP as a stream of bytes.
o Each byte of data has a position in the stream.
oIf the sending application program wants a piece of data to be read out of order by the receiving application program., the sending TCP creates a segment and inserts the urgent data at the beginning of the segment.
oThe rest of the segment can contain normal data from the buffer
o
TCP SEGMENT FORMAT

## Slide 44
Urgent data :
oThe urgent pointer field in the header (if its set) defines the end of the urgent data and the start of normal data.
oWhen the receiving TCP receives a segment with the URG bit set, it extracts the urgent data from the segment using the value of the urgent pointer, and delivers them, out of order, to the receiving application program.
TCP SEGMENT FORMAT

## Slide 45
The client sends the first segment, a SYN segment, in which only the SYN flag is set.
  This segment is for synchronization of sequence numbers. It consumes one sequence
number.
  When the data transfer starts, the sequence number is incremented by 1.
  The SYN segment carries no real data
The server sends the second segment, a SYN +ACK segment, with 2
flag bits set: SYN and ACK.
  This segment has a dual purpose. It is a SYN segment for communication in the other direction and serves as the acknowledgment for the SYN segment.
  It consumes one sequence number.
THREE-WAY HANDSHAKING PROCESS

## Slide 46
The client sends the third segment. This is just an ACK segment.
  It acknowledges the receipt of the second segment with the ACK flag
and acknowledgment number field.
  The sequence number in this segment is the same as the one in the SYN segment.
 The ACK segment does not consume any sequence numbers.
THREE-WAY HANDSHAKING PROCESS

## Slide 48
Any of the two parties involved in exchanging data (client or server) can close
the connection using three-Way Handshaking

## Slide 49: D. F L O W C O N T R O L
TCP uses a sliding window to handle flow control. TCP sliding window is of variable size.
The window is opened, closed, or shrunk.
Opening a window means moving the right wall to the right.
Closing the window means moving the left wall to the right.
Shrinking the window means moving the right wall to the left.
The size of the window at one end is determined by the lesser of two values: receiver window (rwnd) or congestion window (cwnd).

## Slide 50
In computer networking, the Stream Control Transmission Protocol (SCTP) is a transport-layer protocol, serving in a similar role to the popular protocols TCP and UDP. It is standardized by IETF in RFC 4960.
SCTP

## Slide 51: SCTP
SCTP adds to the mix is multi-homing. Multi-homing allows the
two endpoints of a connection to declare multiple interfaces (IP
addresses). Providing and alternate route for the data in case the current interface in use fails for some reason.
The second feature is multi-streaming. Rather than use a single
stream of data, SCTP can create multiple streams that can be used independently.
This doesn’t really improve the speed of the medium but it allows
the data to arrive concurrently; minimizing the wait time for
pages to completely load. This feature also prevents control
packets from getting blocked by data packets, like what usually happens in TCP; thereby improving data control.
TCP’s 3-way handshake initiation, SCTP uses a 4-way handshake that allocates resources near the end of the entire handshake

## Slide 52: SCTP
Data in TCP comes in packets. Packets have a specific size and a long stream would be divided to fit while short ones are spliced together. This means that message framing must be provided at the application layer to fully identify separate messages. SCTP implements message framing and each message would always have the same size when it comes out as it came in.
Summary:
SCTP is better at multi-homing than TCP
SCTP has multi-streaming while TCP doesn’t
SCTP has initiation protection while TCP doesn’t
SCTP has message framing while TCP doesn’t
Ordered delivery is optional with SCTP but not with TCP